## Slide 1: Property-based Testing of Embedded Systems
John Hughes

## Slide 2: What is Property-based Testing?
Traditional automated testing
Execution on SUT
Test case
Expected results
Property-based testing
Execution on SUT
Test case generator
Property of results
Test oracle
Specification
QuickCheck
eqc
+ many others
Notes: Random generation to provoke faults (often ones you wouldn’t think of)
Shrinking to diagnose faults; minimality  relevance

## Slide 3: Systems with state
?
?
?
?
?
?
?
?
int size(Queue *q)
{ return (q->inp - q->outp) % q -> size;
}
Example: circular buffer
q:new(1) -> {ptr, "Queue", 1959398271824}
q:put({ptr, "Queue", 1959398271824}, 0) -> ok
q:get({ptr, "Queue", 1959398271824}) -> 0
q:put({ptr, "Queue", 1959398271824}, 0) -> ok
q:size({ptr, "Queue", 1959398271824}) -> -1
Not modulo: remainder
+ q->size
0 - 1 % 2
Notes: Very general idea.
Key question: what is a test case?
Example: circular buffer implementing a queue
Note: minimal example presented, shrunk from test case of 36 steps

## Slide 4: Testing Safety PLCs
Thonnessen, D., Smallbone, N., Fabian, M. et al (2019). Testing Safety PLCs Using QuickCheck. IEEE International Conference on Automation Science and Engineering, 2019
Robot enabled
Emergency stop buttons
Door sensors
Key (override) switch
Motors enabled
Laser enabled
Input and outputs:
Boolean signals, changing over time
input 1 high, wait 500 ms
input 3 high, wait 200 ms
input 2 high, wait 800 ms
input 1 low, wait 200 ms
What is a test case?
Generate 0 ms half the time
Generate transitions likely to stop the system much less often
1000
EStop_Right press, wait 300 ms
Door_Back open, wait 100 ms
EStop_Right release, wait 100 ms
SyTeC
Notes: Contains logic and delays.
Safety for a robot with a laser in an enclosure; stop stuff in an emergency or if door is opened.
NOT random booleans at each instant—would not provoke behaviours like ”if button is pressed for 300ms…”
Shrinking adds delays when deleting a command; can also shrink delays.
On a release, the PC allows everything to be turned back on, despite the open door. Thanks to delays inside the PLC.

## Slide 5
Notes: Testing AutoSAR basic software
For Volvo Cars: Volvo buy components running basic software from different vendors; if they don’t follow the standard, they may not be able to talk to each other.

## Slide 6: How do we model this?
Top-level API
Talks to the hardware driver
CanNm
Make top-level calls
Mock the lower level calls
Check the expected calls are made
Provide return values—inputs to the component
What is a test case step?
An API call, along with expected calls out
Notes: How do we model this? Note each layer is specified separately; want to model one layer at a time.

## Slide 7: How do we test using the models?
CanNm
Top-level calls
Mock lower level calls
CanSm
Top-level calls
Mock lower level calls
Generate a top-level call
Compute expected calls
Use the model to compute results
Compute expected low-level calls
Notes: Implementation just a black box; does not consist of layers!
Clustering models means no implementation of the internal interface is needed.

## Slide 8: A Bug in a vendor’s CAN stack
send priority 1
send priority 2
send priority 3
tx_confirm
sending 1
sending 3
1 sent
CAN bus
queued
Notes: Feature interaction: you cannot test all combincations

## Slide 9: The Problem
CAN bus identifiers determine bus priority

## Slide 10: A Bug in a vendor’s CAN stack
send priority 1
send priority 2
send priority 3
tx_confirm
sending 1
sending 3
1 sent
CAN bus
queued
Failed to mask off the top bit before comparing priorities
Notes: Feature interaction: you cannot test all combincations

## Slide 11
3,000 pages of specifications
20,000 lines of QuickCheck
1,000,000 LOC, 6 suppliers
200 problems
100 problems in the standard
Notes: Does it scale? Yes, it scales.

## Slide 12: Cyberphysical Systems
Combination of discrete and continuous behaviour
Example: adaptive cruise control
  Speed/distance/gas/brake: continuous
  Hitting the car in front: discrete
Running a test  running a simulation: expensive
What is a test case?
Arbitrary data + N real parameters (e.g. wavelength, amplitude…)
Ramezani, Z., Claessen, K., Smallbone, N. et al (2022). Testing Cyber-Physical Systems Using a Line-Search Falsification Method. IEEE Transactions on Computer-Aided Design of Integrated Circuits and Systems, 41(8)
Sometimes random generation is not enough
SyTeC

## Slide 13: Example: Distance to car in front
Chart: 
| 0 | 0.1 | 0.2 | 0.30000000000000004 | 0.4 | 0.5 | 0.6 | 0.7 | 0.79999999999999993 | 0.89999999999999991 | 0.99999999999999989 | 1.0999999999999999 | 1.2 | 1.3 | 1.4000000000000001 | 1.5000000000000002 | 1.6000000000000003 | 1.7000000000000004 | 1.8000000000000005 | 1.9000000000000006 | 2.0000000000000004 | 2.1000000000000005 | 2.2000000000000006 | 2.3000000000000007 | 2.4000000000000008 | 2.5000000000000009 | 2.600000000000001 | 2.7000000000000011 | 2.8000000000000012 | 2.9000000000000012 | 3.0000000000000013 | 3.1000000000000014 | 3.2000000000000015 | 3.3000000000000016 | 3.4000000000000017 | 3.5000000000000018 | 3.6000000000000019 | 3.700000000000002 | 3.800000000000002 | 3.9000000000000021 | 4.0000000000000018 | 4.1000000000000014 | 4.2000000000000011 | 4.3000000000000007 | 4.4000000000000004 | 4.5 | 4.5999999999999996 | 4.6999999999999993 | 4.7999999999999989 | 4.8999999999999986 | 4.9999999999999982
distance | 11.25 | 10.76 | 10.29 | 9.84 | 9.41 | 9 | 8.61 | 8.24 | 7.89 | 7.56 | 7.25 | 6.96 | 6.69 | 6.44 | 6.21 | 6 | 5.81 | 5.64 | 5.49 | 5.36 | 5.25 | 5.16 | 5.09 | 5.04 | 5.01 | 5 | 5.01 | 5.04 | 5.09 | 5.16 | 5.25 | 5.36 | 5.49 | 5.64 | 5.81 | 6 | 6.21 | 6.44 | 6.69 | 6.96 | 7.25 | 7.56 | 7.89 | 8.24 | 8.61 | 9 | 9.41 | 9.84 | 10.29 | 10.76 | 11.25
Chart: 
| 0 | 0.1 | 0.2 | 0.30000000000000004 | 0.4 | 0.5 | 0.6 | 0.7 | 0.79999999999999993 | 0.89999999999999991 | 0.99999999999999989 | 1.0999999999999999 | 1.2 | 1.3 | 1.4000000000000001 | 1.5000000000000002 | 1.6000000000000003 | 1.7000000000000004 | 1.8000000000000005 | 1.9000000000000006 | 2.0000000000000004 | 2.1000000000000005 | 2.2000000000000006 | 2.3000000000000007 | 2.4000000000000008 | 2.5000000000000009 | 2.600000000000001 | 2.7000000000000011 | 2.8000000000000012 | 2.9000000000000012 | 3.0000000000000013 | 3.1000000000000014 | 3.2000000000000015 | 3.3000000000000016 | 3.4000000000000017 | 3.5000000000000018 | 3.6000000000000019 | 3.700000000000002 | 3.800000000000002 | 3.9000000000000021 | 4.0000000000000018 | 4.1000000000000014 | 4.2000000000000011 | 4.3000000000000007 | 4.4000000000000004 | 4.5 | 4.5999999999999996 | 4.6999999999999993 | 4.7999999999999989 | 4.8999999999999986 | 4.9999999999999982
distance | 6.75 | 6.26 | 5.79 | 5.34 | 4.91 | 4.5 | 4.11 | 3.74 | 3.39 | 3.06 | 2.75 | 2.46 | 2.19 | 1.94 | 1.71 | 1.5 | 1.31 | 1.14 | 0.99 | 0.86 | 0.75 | 0.66 | 0.59 | 0.54 | 0.51 | 0.5 | 0.51 | 0.54 | 0.59 | 0.66 | 0.75 | 0.86 | 0.99 | 1.14 | 1.31 | 1.5 | 1.71 | 1.94 | 2.19 | 2.46 | 2.75 | 3.06 | 3.39 | 3.74 | 4.11 | 4.5 | 4.91 | 5.34 | 5.79 | 6.26 | 6.75
Chart: 
| 0 | 0.1 | 0.2 | 0.30000000000000004 | 0.4 | 0.5 | 0.6 | 0.7 | 0.79999999999999993 | 0.89999999999999991 | 0.99999999999999989 | 1.0999999999999999 | 1.2 | 1.3 | 1.4000000000000001 | 1.5000000000000002 | 1.6000000000000003 | 1.7000000000000004 | 1.8000000000000005 | 1.9000000000000006 | 2.0000000000000004 | 2.1000000000000005 | 2.2000000000000006 | 2.3000000000000007 | 2.4000000000000008 | 2.5000000000000009 | 2.600000000000001 | 2.7000000000000011 | 2.8000000000000012 | 2.9000000000000012 | 3.0000000000000013 | 3.1000000000000014 | 3.2000000000000015 | 3.3000000000000016 | 3.4000000000000017 | 3.5000000000000018 | 3.6000000000000019 | 3.700000000000002 | 3.800000000000002 | 3.9000000000000021 | 4.0000000000000018 | 4.1000000000000014 | 4.2000000000000011 | 4.3000000000000007 | 4.4000000000000004 | 4.5 | 4.5999999999999996 | 4.6999999999999993 | 4.7999999999999989 | 4.8999999999999986 | 4.9999999999999982
distance | 5.75 | 5.26 | 4.79 | 4.34 | 3.91 | 3.5 | 3.11 | 2.74 | 2.39 | 2.06 | 1.75 | 1.46 | 1.19 | 0.94 | 0.71 | 0.5 | 0.31 | 0.14 | -0.01 | -0.14 | -0.25 | -0.34 | -0.41 | -0.46 | -0.49 | -0.5 | -0.49 | -0.46 | -0.41 | -0.34 | -0.25 | -0.14 | -0.01 | 0.14 | 0.31 | 0.5 | 0.71 | 0.94 | 1.19 | 1.46 | 1.75 | 2.06 | 2.39 | 2.74 | 3.11 | 3.5 | 3.91 | 4.34 | 4.79 | 5.26 | 5.75
FAIL
PASS
PASS
Optimisation
Distance to False:
5
0,5
0

## Slide 14: ”Valued Booleans”
(True, 5)
distance to False
(True,d1) && (True,d2) = (True, 1 )
1
1
+
d1
d2
(True, 5) && (True, 0.5) = (True, 45/99)
(True, 4) && (True, 0.5) = (True, 44/99)
(True, 5) && (True, 0.4) = (True, 370/999)

## Slide 15: ”Line Search”
Search for a zero:
Chart: 
| 1 | 2 | 3
f | 10 | 12 | 15
Chart: 
| 1 | 2 | 3
f | 15 | 12 | 10
Chart: 
| 1 | 2 | 3
f | 15 | 12 | 13
In RN, switch now and then to a line in a random direction through the current point

## Slide 16
Notes: Uniform random is the worst… but solves some examples well.
Hybrid corner-random (uniform half the time, extremal values half the time) works surprisingly well for easy examples
* Beyond about 200 simulations (i.e. for harder examples), line-search is överlägset.

## Slide 17
Notes: If we confine our attention to those problems where optimisation is needed to find a counterexample: LSF looks even better.

## Slide 18: Three settings for PBT of embedded systems
Exploit a specification without any proofs
What is a test case?
How to generate, shrink, or optimise them
Finds failing tests you would never have thought of
Notes: We’ve seen PBT in three settings.
What can we learn?

## Slide 19
Don’t write tests
Generate them!